## Slide 1
Funding Opportunities for EV Infrastructure
Ashland County Charges Ahead
Cheq Bay Renewables
Clam Lake DCFC

## Slide 2
Homeowner
Business
Municipality
Nonprofit
Tribe
Funding depends on who you are

## Slide 3
Xcel
EV Accelerate at Home
Commercial Program Credits
Bayfield Electric
Rebates
Dahlberg
New Programs in Development
Incentives depend on your utility

## Slide 4
Residential Level-2
10kW $620
19kW $2000
Commercial Level-2
15kW Pedestal with Card Reader $10,600
Commercial Level-3
150kW $97,300
Charging Equipment (EVSE) costs vary by capacity and features

## Slide 5
Residential Level-2
240v available $200
Upgrade service $2000
Commercial Level-2
Site dependent $2000 - $10,000
Commercial Level-3
Site Dependent - $80K to $120K
Installation costs also vary by EVSE capacity and site

## Slide 6
Electric Bill
Energy Charges (kWh)
Monthly Fees
Cellular Plan
Credit Card Fees
Operations & Maintenance
Contract with EVSE Vendor
Demand Charges (kW)
Costs continue after installation

## Slide 8: Funding
1) Tax Credits
2) Utility Programs
3) Grants
Grants
Utility Programs
Tax Credits

## Slide 9: Tax Credits
PART 1

## Slide 10
Instructions for Form 8911 (01/2023) | Internal Revenue Service (irs.gov)

## Slide 11: Homeowner Alternate Fuel Tax Credit
Must be in eligible census tract (disadvantaged)
  20% poverty rate or greater, or
  80% of State median income
Maximum credit smaller of 30% or $1000
Ashland County Disadvantaged Areas (Grey)

## Slide 12: Ashland County Census Tracts
50400 Eligible
50800 Eligible

## Slide 13: Ashland County Census Tracts
50300 Not Eligible
50500 Not Eligible

## Slide 14: Ashland County Census Tracts
50600 Eligible
50700 Eligible

## Slide 15: Business Alternate Fuel Tax Credit
6% tax credit not to exceed $100K
May be eligible for 30% if wage and apprenticeship requirements met
Must be in eligible census tract, OR
Is NOT an urban area
Ashland County Disadvantaged Areas (Grey)
Federal Register :: 2020 Census Qualifying Urban Areas and Final Criteria Clarifications

## Slide 16: Elective Pay Alternate Fuel Tax Credit
Municipalities, nonprofits, and tribes and now claim tax credit(s)
Use same rules as a business
Previously called Direct Pay
Also applies to renewable energy projects

## Slide 17: Utility Programs
Part 2

## Slide 18: Utility EVSE Programs for Homeowners
Bayfield electric cooperative
Rebate for home chargers
  $400 EVSE
  $800 Smart EVSE with internal meter
  Both options are on load control program
Additional programs in development
Xcel Energy
“EV Accelerate at Home”
  EVR-1 tariff
  Must be under Residential (Rg-1) or Farm Service (Fg-1)
  Residential Time-of-Day (Rg-2) or Parallel Generation (Pg-1) is not eligible

## Slide 19: Xcel Residential EV Accelerate at Home Rates

## Slide 20: Xcel Program Chargers

## Slide 21: Xcel Program Costs/Pricing

## Slide 22: Residential EVSE Comparison – Initial Installation
Charger | EVSE | EVSE Setup | 240v to Charger | Utility Rebate | Tax Credit (if eligible) | Total
Xcel - EVR-1 JuiceBox 40a, 9.6kW | $780 | Included | $500? |  | ($384) | $896
Xcel – Rg-1 JuiceBox 40a, 9.6kW | $617 | $150 | $500? |  | ($380) | $887
Bayfield Electric – JuiceBox 40a, 9.6kW | $617 | $150 | $500? | ($800) | ($140) | $327

## Slide 23: Residential EVSE Comparison – After Installation
Utility Tariff | Annual Miles Driven | Annual kWh | Annual kWh $ if Charge at Night or Weekends
Xcel - EVR-1 EV Sedan | 15,000 | 3,750 | $253
Xcel – Rg-1 EV Sedan | 15,000 | 3,750 | $499
Bayfield Electric Cooperative EV Sedan | 15,000 | 3,750 | $480
Xcel or BEC with 3.1 kW Solar PV | 15,000 | 3,750 | $0

## Slide 24: Xcel’s Commercial EV Program (EVC-1)
Embedded Program Credits
Off-peak Rates
Demand Charges
  Demand Limiters

## Slide 25: Xcel’s Commercial EV Program (EVC-1)
Embedded Program Credits - Example
Total Cost 4-port L2 & L3 | Grant 80% | Cost Share 20% | Xcel Program Credit | Cost to Site Owner
$276,553 | ($221,243) | ($55,311) | ($58,097) | $0

## Slide 26: Xcel’s Commercial EV Program (EVC-1)
Off-peak Rates – Example Bayfield County Fleet 2022
 | Miles driven | 2022 cost of gasoline ($3.60/gal) | Cost of off-peak electricity equivalent ($0.056/kWh) | 2022 EV Savings %
Bayfield County fleet | 345,900 | $41,508 | $4,843 | 88%

## Slide 27: Xcel’s Commercial EV Program (EVC-1)
Demand Charges
  - Demand Limiters
4-port Station | Capacity kW | Demand Charge On-peak Summer ($13/kW) | Adjusted Demand 150 Limiter | Adjusted Demand Charge
2 L3 & 2 L2 | 330 | $4290 | 12 (1800kWh/150) | $156
Charging Station | Monthly Hours Used | kWh Used
Two L3 150kW | 10 | 1500
Two L2 15kW | 20 | 300
Total |  | 1800
Revenue at $0.30/kWh |  | $540

## Slide 28: CBR Tool
Enter EVSE capacity and estimated hours used – results Xcel electric bill and rate per kWh:
ev_charging_electric_bill_analysis_xcel.v5protected.xlsx (live.com)

## Slide 29: GRANTS
Rural EV Toolkit: Rural EV Toolkit (PDF Version) | US Department of Transportation
Funding Table: Rural EV Infrastructure Funding Table (PDF Version) | US Department of Transportation
Funding Table: Rural EV Funding Table.xlsx (live.com)
80 Grant or Loan Programs Listed

## Slide 31: List of some Grants for EVSE
Municipalities and tribes
U.S. Department of Transportation – Charging and Refueling Infrastructure (CFI)
WI Department of Transportation – Wisconsin Electric Vehicle Infrastructure (WEVI) (Next month topic)
VW Funds – Through State of WI, details TBD
Nonprofits
EVs for Good - EVs for Good - RENEW Wisconsin
farms and rural business
USDA Rural Energy for America Program (REAP)

## Slide 32: U.S. DOT (FHWA) CFI Grant
$700M in two separate categories
  $350M Corridor Program,
  $350M Community Program
Either program must comply with NEVI Standards and Requirements
  4-port minimum
  Public access
  Contactless payment methods
  Connector types
  Etc.

## Slide 33: FWHA Priorities
  Safety
  Carbon Reduction
  Equity & Justive40
  Workforce Development
  Accessibility

## Slide 34: DOT CFI Highlights
Eligible applicants
States
Local units of government
Tribes
Few details
80% grant/ 20% cost share
All aspects of an EVSE project are eligible expenses
Community Program can use funds for secondary roads
Minimum grant $500K, maximum $15M

## Slide 35: DOT CFI Grant Writing Components
  Extensive narrative requirements
  Budget information
  Project Merit Criteria
    Safety
    Climate Change
    Equity, Community Engagement, and Justice40
    Workforce Development, Job Quality and Wealth Creation
    CFI Program Vision
  Project Readiness and Environmental Risk

## Slide 36: DOT CFI GRANT WRITING
Who is going to take the lead?
  Narrative research and writing: 80-100 hours (or more?)
  Community engagement: 40 hours (or more?)
    Town meeting
    City Council meeting
    County Board meetings
    Various committee meetings
    Meeting with site hosts
  Engage with utilities: 10-15 hours

## Slide 37: DOT CFI Example – Bayfield County Submitted June 13, 2023
Key ingredients
11 sites with 4 ports each
Mix of Level-2 and Level-3 chargers
All sites in Xcel Energy territory
Xcel’s commercial EV tariff (EVC-1) has Program Credits which covers the 20% cost share
Xcel has “demand limiter” formula in tariffs to reduce demand charges for small usage
results
Ownership transfers from Bayfield County to 11 site owners
No cost to site owners
First 5-years of O&M covered by project
Electric bills covered by paying customers
One L2 charger used one hour/day = $22K in annual economic benefit to community

## Slide 38
Bayfield County DOT CFI Budget
Site Description | Engineering & Distribution | EV Supply Infrastructure (EVSI) | EV Supply Equipment (EVSE)+O&M | Safety Equipment. ADA Compliance | County Administration | Contingency | Site Total
Ashland | $26,500 | $74,900 | $224,121 | $7,860 | $4,000 | $34,868 | $383,544
Bayfield | $18,500 | $74,900 | $136,387 | $5,860 | $4,000 | $25,141 | $276,553
Cable | $19,000 | $74,900 | $136,387 | $5,860 | $4,000 | $25,191 | $277,103
Cornucopia | $12,500 | $74,900 | $136,387 | $5,860 | $4,000 | $24,541 | $269,953
Drummond | $14,500 | $74,900 | $136,387 | $6,360 | $4,000 | $24,791 | $272,703
Grandview | $8,500 | $74,900 | $136,387 | $5,860 | $4,000 | $24,141 | $265,553
Herbster | $2,000 | $74,900 | $136,387 | $5,860 | $4,000 | $23,491 | $258,403
Lakewood | $13,750 | $74,900 | $136,387 | $5,860 | $4,000 | $24,666 | $271,328
Red Cliff | $5,000 | $74,900 | $136,387 | $7,860 | $4,000 | $23,991 | $263,903
Washburn | $9,500 | $74,900 | $224,121 | $7,860 | $4,000 | $33,168 | $364,844
Port Wing | $25,500 | $74,900 | $136,387 | $6,360 | $4,000 | $25,891 | $284,803
Subtotal | $155,250 | $823,900 | $1,675,725 | $71,460 | $44,000 | $277,034 | $3,047,369
% of Total | 5.1% | 27.0% | 55.0% | 2.3% | 1.4% | 9.1% | 100%

## Slide 39
Bayfield County DOT CFI Budget (continued)
Site Description | Total with Contingency | Grant Request 80% | 20% Cost Share Requirement | Est. Xcel Program Credit | Excess Program Credit | Site Owner NET COST ESTIMATE
Ashland | $371,119 | ($296,895) | ($74,224) | ($96,232) | ($22,008) | $0.00
Bayfield | $263,612 | ($210,889) | ($52,722) | ($58,394) | ($5,672) | $0.00
Cable | $264,162 | ($211,329) | ($52,832) | ($58,394) | ($5,562) | $0.00
Cornucopia | $257,012 | ($205,609) | ($51,402) | ($58,394) | ($6,992) | $0.00
Drummond | $259,762 | ($207,809) | ($51,952) | ($58,394) | ($6,442) | $0.00
Grandview | $252,612 | ($202,089) | ($50,522) | ($58,394) | ($7,872) | $0.00
Herbster | $245,462 | ($196,369) | ($49,092) | ($58,394) | ($9,302) | $0.00
Lakewood | $258,387 | ($206,709) | ($51,677) | ($58,394) | ($6,717) | $0.00
Red Cliff | $250,962 | ($200,769) | ($50,192) | ($58,394) | ($8,202) | $0.00
Washburn | $352,419 | ($281,935) | ($70,484) | ($96,232) | ($25,748) | $0.00
Port Wing | $271,862 | ($217,489) | ($54,372) | ($58,394) | ($4,022) | $0.00
Total | $3,047,369 | ($2,437,895) | ($609,474) | ($718,014) | ($108,540) | $0.00

## Slide 40
Bayfield County’s only disadvantaged census tract

## Slide 41: Community Engagement
Bayfield County Executive Committee, May 11, 2023
Bayfield County Board of Supervisors, May 30, 2023
Town of Bell, May 9, 2023
Town of Clover, April 25, 2023
Town of Port Wing, April 28, 2023 and June 5, 2023
Town of Grandview, May 10, 2023
Town of Drummond, May 9, 2023
Town of Namakagon, June 13, 2023
City of Bayfield, May 11 Public Works, May 17 City Council
City of Washburn, May 8, 2023 City Council
City of Washburn June 12, 2023 City Council
Red Cliff Planning administration, various dates and initiatives
Lots of meeting and time spent

## Slide 42
Workforce Development – Another key grant focus
Entity | Job Description | Number of Jobs
Xcel Energy | Engineer/Design | 2
 | Project Manager | 1
 | Construction Crew | 4-6
 | Administration | .5
EVSE Vendor | Project Manager | 1
 | Manufacturing jobs | 3-4
 | EVSE Technician | 1
Bayfield County | Project Manager/Reporting | .75
Red Cliff | Casino Maintenance/Reporting | .25
Other Site Owners | Maintenance/Reporting | .25 *10
Total Jobs Created or Sustained |  | 16-20
Jobs Created or Sustained

## Slide 43: Bayfield County DOT CFI Application
Link to read application narrative:
project_narrative_final_mergedv8.pdf (cheqbayrenewables.org)

## Slide 44
Homeowner EVSE Flowchart
Legend:
BEC – Bayfield Electric Co-op
Rg-1 Residential Service
EVR-1 Electric Vehicle Residential
In Summary:

## Slide 45
Business
Utility – Xcel Energy
Funding Sources
Legend:
Cg-2 Small General Service
Cg-7 General Service Time of Day
EVC-1 Electric Vehicle Commercial

## Slide 46
Business
Utility = Bayfield Electric
Funding Sources

## Slide 47: Thank You
From Cheq Bay Renewables
Bill Bailey
billebailey2@gmail.com
www.cheqbayrenewables.org